Model：SH-40

2D Barcode scanner engine

SH-40 uses advanced imaging technology, has a very strong bar code scan and digital image acquisition function to realize the long depth of field and fast reading, and enhance the literacy of low quality bar code. From the universal one dimensional bar code to the two-dimensional bar code on the mobile device screen, SH-40 can read easily.

The new high integrated design and reliability design, the key parts of the internal components are installed on a fixed module, suitable for mobile, device cabinet, assembly line, intelligent machine equipment integration.

Product features

Unique decoding technology： high performance decoding technology is used to decode various one-dimensional and two-dimensional codes to achieve fast and accurate scanning.

High performance scanning technology: supporting all kinds of damaged and deformed bar code scanning, and supporting the scanning of two-dimensional code of computer, mobile phone and flat screen.

Widely used devices: ultra small volume, widely used mobile handheld terminals, POS payment, equipment cabinet, intelligent robot and other IOT industrial chain.

Scanning performance

Barcode 					 scan depth density

5mil Code39                 40-90mm

6.67mil PDF417              30-130mm

10mil Data Matrix            50-90mm

13mil EAN-13                50-200mm

20mil QR Code               25-240mm

This data may vary due to barcode quality and environmental factors.

SH-40 Technical parameters

Scanning performance

Sensor                       640×480 CMOS

Lighting                      White light LED

Focusing                     Red light LED

Symbologies  2D            QR Code, Data Matrix, PDF417,Aztec, Maxicode，Hanxin

EAN,UPC,Code 39,Code 93,Code 128,UCC/EAN 128, Codabar，

Interleaved 2 of 5, ITF-6,ITF-14,ISBN,ISSN, MSI-Plessey

1D             GS1 Databar,GS1 Composite Code,Code 11,Industrial 25,

Standard 25,Plessey,Matrix 2 of 5

Accuracy of recognition      ≥5mi

Read the depth of field	EAN-13 	50mm-200mm (13mil)

Code39	40mm-90mm（5mil 10 bytes）

QR Code 	25mm-240mm (20mil 16 bytes)

Data Marix	50mm-90mm（10mil 20 bytes）

PDF 417 	30mm-130mm (6.67mil 7 bytes)

Scanning angle              The rotation angle is 360 degrees, the elevation angle is 55 degrees, the angle of the deflection is + 55 degrees.

Field angle                   Level 34 degrees, vertical 26 degrees

Contrast ratio                ≥25%

Mechanical / electrical parameters

Communication interface     TTL-232 , USB (HID-KBW、虚拟串口)

Appearance size              26(W)×15.3(D)×14(H)mm

working voltage              DC 3.3 V

Working current              170mA

Standby current               USB 25mA;串口2uA

Environmental parameters

Working temperature         -20℃~+50℃

Storage temperature          -40℃~+70℃

Working humidity             5%~95%（No condensation）

Environmental illumination     0~100000LUX

| Mechanical dimension drawing | Diagram of 12Pin line connection |
| --- | --- |
|  | The FPC connector is double-sided contact. See the table below for the definition of the specific sequence |
| Line sequence definition |
| PIN | PIN Input/output | definition | state |
| PIN 1 | － | NC | dangling |
| PIN 2 | power supply | VCC | + 3.3 V input |
| PIN 3 | land | GND | － |
| PIN 4 | Input | RX | Serial port receiver signal |
| PIN 5 | output | TX | Serial port sending terminal signal |
| PIN 6 | Input | D- | USB port is D- signal |
| PIN 7 | output | D+ | The USB port is D+ signal |
| PIN 8 | － | NC | － |
| PIN 9 | output | BEEPER | Passive buzzer output signal, idle low level |
| PIN10 | output | DLED | Decode successfully prompt light, idle low level |
| PIN11 | － | NC | － |
| PIN12 | Input | TRIG | Weak pull up, low level trigger engine decoding |

ScanHome

ShangHai ScanHome Technology Co.,Ltd

Tel:  8621-67879985

Mail:  scanhome@163.com

http:  www.scanhome.net

Add: 	5thFloor,Buidings5,NO.68,ZhongchuangRoad,Songjiang District,Shanghai,China    Zip:  201613